## Slide 1: Efficient Allocation of Renewable Energy Sources under Uncertainty in the UK

## Slide 2: The Problem - Renewables
The climate crisis is ever increasing the focus on renewable energy sources around the world.
However, many of the prevalent renewable energy sources (e.g. wind and solar) are reliant on an inconsistent factor, the weather.
In the UK, the average load factor (percentage of overall capacity output) per year of onshore wind is 26.46% in 2019, with performing better at 40.4% (Jaganmohan, 2019)
Chart: UK Renewable Energy Generation 2021
| Wind | Shoreline wave / tidal | Solar PV | Hydro | Landfill gas | Sewage sludge digestion | Other biomass (inc. co-firing) [note 14]
 | 43049 | 0 | 11450.03 | 153.76 | 2911.36 | 984.31 | 30767.46
(Department for Business, Energy & Industrial Strategy, 2022)

## Slide 3: The Problem - Allocation
Due to this uncertainty in output, the decision of where to allocate a budget of new energy sources can be difficult.
On top of this, when considering a country wide scale the number of potential candidate locations can be huge leading to another problem – how do you make an efficient decision balancing a range of factors?
This project is proposing an AI based approach to tackle both the problem of uncertainty and scale of allocating a budget for new energy sources across the UK.

## Slide 4: Background Research
Before beginning this project, we required some initial information to base our decisions upon.
Mainly:
  Types of renewable sources to investigate,
  Factors affecting different generation types,
  Costs,
  Location suitability,
  Where to source data from

## Slide 5: Constraints & Scope Restrictions
Based upon background research, to keep the project feasible we narrowed the scope to focus on specific areas:
  Consider only the allocation of a budget of Wind Turbines as they are more location dependent than alternatives such as solar and much more suitable for large scale use.
  Limit to onshore wind farm allocation as comprehensive weather information (for a training set) is not as readily available for locations out at sea.
  Initially demonstrate allocation to locations with pre-existing windfarms as location eligibility introduces large amounts of complexity with construction permits and such.
  We believe these limitations will still allow us to demonstrate a proof of concept that can be expanded to more general cases in future work.

## Slide 6: Solution Overview
Our approach can be broken up into three sections:
  Training a general wind turbine generation model based upon predicted or recorded weather features.
  For each of our locations, producing a statistical model of the weather (based off long term past weather information) allowing us to produce a sample of ‘expected’ for each location.
  Using the above two steps to calculate the performance of a given allocation, and to search for an allocation that will maximise a set of performance objectives.

## Slide 7: Location Selection
The main requirements for location candidacy here was the availability of data to form a training and testing set.
We pulled from a dataset on the National Grid ESO data website, giving us a list of unique IDs for UK wind farms.
This then underwent a couple of cuts removing offshore wind farms, and any locations where past generation data was not consistently available leaving us with the following locations.
Coincidentally they are all located in Scotland which adds another constraint to our investigation.

## Slide 8: Data Collection
To train our model we needed a dataset consisting of 2 parts for a large set of points in time:
  Historical Weather data with a range of features
  The actual generation of a location compared to its maximum capacity.
We were able to source these from two locations, VisualCrossing.com and the Elexon Balancing Mechanism Reporting Service. Giving us access to historical records at 30-minute intervals.

## Slide 9: Data Collection – The Dataset
 | BMUID | temp | windspd | windgust | sealevelpressure | visibility | cloudcover | precip | dew | humidity | loadFactor
0 | ABRTW-1 | 5.5 | 11.6 | 15.5 | 1008.1 | 12.1 | 86.3 | 0 | 3.9 | 89.4 | 0.697666667
1 | ABRTW-1 | 4.1 | 22.2 | 30.8 | 969.9 | 3.8 | 86.2 | 0 | 2.5 | 89.1 | 0.667611111
2 | ABRTW-1 | 8.6 | 4.4 | 6 | 1028.8 | 39 | 38.6 | 0 | 1.6 | 61.48 | 0.071444444
3 | ABRTW-1 | 17 | 7.6 | 6.9 | 1014.6 | 33.8 | 4.8 | 0 | 5.4 | 46.24 | 0.053333333
4 | ABRTW-1 | 13.7 | 11.8 |  | 1019.3 | 23.6 | 76.8 | 0 | 10.2 | 79.66 | 0.331277778
5 | ABRTW-1 | 22.6 | 13.4 |  | 1013.5 | 33.6 | 36.2 | 0 | 10.6 | 46.81 | 0.279888889
6 | ABRTW-1 | 7.6 | 25.7 | 30 | 1015.7 | 26.2 | 29.6 | 0 | 6.3 | 92 | 0.892222222
7 | ACHRW-1 | 3.8 | 13.5 | 12.6 | 1008.3 | 23.5 | 39.4 | 0 | 2.7 | 92.44 | 0.126525822
8 | ACHRW-1 | 3.4 | 19.6 | 22.1 | 969.4 | 4.5 | 51.8 | 0 | 1.6 | 87.85 | 0.598028169
9 | ACHRW-1 | 6 | 13.7 | 19 | 1029.9 | 29.7 | 23.8 | 0 | 1 | 70.48 | 0.228497653
10 | ACHRW-1 | 16.4 | 7.8 | 6.2 | 1014.8 | 35.2 | 35.4 | 0 | 4.4 | 44.87 | 0.062488263
11 | ACHRW-1 | 12.2 | 10.7 |  | 1018.4 | 9.3 | 61.5 | 0 | 11.8 | 97.56 | 0.082769953
12 | ACHRW-1 | 14.6 | 10 | 14.2 | 1014.3 | 32.2 | 45.9 | 0 | 9.6 | 72.2 | 0.386244131
13 | ACHRW-1 | 7 | 18.2 | 18.6 | 1014.4 | 9.3 | 67.1 | 0 | 5.5 | 90.17 | 0.749671362
14 | AKGLW-2 | 4.3 | 9.2 |  | 1007.2 | 26.9 | 33.3 | 0 | 3.1 | 92.31 | 0.64924812
15 | AKGLW-2 | 3.6 | 22.7 | 31.1 | 969.1 | 11.5 | 80.7 | 0 | 2.2 | 90.64 | 0.850407268
16 | AKGLW-2 | 8.4 | 6 |  | 1028.5 | 29.1 | 70.6 | 0 | -0.1 | 55.08 | 0.033364662
17 | AKGLW-2 | 9.7 | 12.3 |  | 1016.5 | 20.7 | 23.6 | 0 | 6.2 | 79.02 | 0.056453634
18 | AKGLW-2 | 11.9 | 4.2 |  | 1019.9 | 20.3 | 20.9 | 0 | 11.4 | 97.3 | 0.529573935
  Using these sources, we constructed a 7000+ entry dataset of weather features and the percentage of maximum capacity output during that same period.

## Slide 10: Prediction Model
From this dataset we can visualise the correlation between different features.
A range of different regression models were tested, from standard linear regressors to MLP and gradient boosting variants.

## Slide 11: Prediction Model - TPOT
After tuning hyperparameters of a gradient boost model and still not being 100% satisfied with the accuracy we discovered a meta-learning library called TPOT.
This allowed us to find a pipeline of different models combined to improve the performance further using the following model.
exported_pipeline = make_pipeline(
StackingEstimator(estimator=ExtraTreesRegressor(bootstrap=False, max_features=0.55, min_samples_leaf=1, min_samples_split=5, n_estimators=100)),
StackingEstimator(estimator=ExtraTreesRegressor(bootstrap=False, max_features=0.55, min_samples_leaf=9, min_samples_split=8, n_estimators=100)),
VarianceThreshold(threshold=0.01),
StackingEstimator(estimator=AdaBoostRegressor(learning_rate=0.001, loss="linear", n_estimators=100)),
SelectPercentile(score_func=f_regression, percentile=28),
StackingEstimator(estimator=LinearSVR(C=0.5, dual=False, epsilon=0.0001, loss="squared_epsilon_insensitive", tol=0.01)),
StackingEstimator(estimator=GradientBoostingRegressor(alpha=0.95, learning_rate=0.01, loss="lad", max_depth=7, max_features=1.0, min_samples_leaf=9, min_samples_split=10, n_estimators=100, subsample=0.5)),
StackingEstimator(estimator=LinearSVR(C=20.0, dual=True, epsilon=0.001, loss="epsilon_insensitive", tol=1e-05)),
KNeighborsRegressor(n_neighbors=61, p=2, weights="distance")
)

## Slide 12: The Allocation
Due to the uncertain aspects of the weather, we expect quite a variation in the no matter the allocation.
In an ideal world we want to find an allocation that maximises the mean output of our proposed new wind turbines (ideally improving on the current average load factor) while also minimising the variance in the outputs.
To do this we could combine these values as a weighted sum and use it as a performance heuristic for a searching algorithm.
This would require us to determine the relative importance of each aspect.

## Slide 13: The Allocation – Genetic Algorithms
An alternate approach is to use a Genetic Algorithm based approach.
The NGSA-II algorithm published in 2002 gives a fast search methodology based around ranking its populations based on dominating fronts and crowding distances.
This algorithm is not state of the art anymore with many different improvements being published, but as a baseline it is provenly reliable and showed much room for expansion by slight changes – opening a clear route to performance improvements in future works.

## Slide 14: The Allocation – Genetic Algorithms
There are some trade-offs to make with this approach, namely search time.
The time taken to iterate through a 100 generations of a population can be time consuming, but you also need to consider a range of initial random starts as that will impact the search space.
Considering this time cost, we do not think this is too much of a price to pay in this context as in most cases this will be ran fully to obtain recommendation irregularly.

## Slide 15: Results
When testing with a range of initial seeds, we see the algorithm trend towards a higher mean every generation, but usually caps around the 30% load factor.
This is already theoretically an improvement over the average across the UK currently.
However, this value shouldn’t be taken at face value. Throughout the chain of operations, we can find small errors that will likely add to an inaccuracy of this result.

## Slide 16: “The Efficient Allocation”
Under the preconditions of our 56 locations being eligible candidates and a proposed budget to allocate a maximum of 50 new turbines across these locations we are returned the following distributions.
We can see that the allocations are very sparce with a few locations being allocated a small number of turbines while most get none.
Placeholder – will be filled by a heatmap of locations showing the distributions.

## Slide 17: Future Extensions
One of the main extensions I believe would be useful in future would be adjusting the current setup to be more general.
Currently we require a backlog of data for each location we want to predict for which can make it more complex to query the system for a new location.
I would also like to investigate extensions to the NSGA-II algorithm as increasing performance would make this much more scalable for larger location sets.